## Slide 1: Autonomous Navigation of a Mars Rover
Harshal Upadhyay
Oct 3, 2022

## Slide 2: Overview
Motivation:
Develop a workshop around AI/Robotics application for Grace Hopper Celebration conference for 2022 (GHC22)
GHC is the world's largest gathering of women technologists featuring a wide variety of sessions including many trending technical tracks.
Rover Mission:
Rover should reach a chosen goal location on a virtual Martian terrain autonomously and capture a soil sample.
Key Capabilities:
Plan an optimal path based on a known terrain map and some known obstacles.
Once an optimal path is found, rover must navigate the uneven terrain, follow the planned path and reach the desired goal location.
Avoid any unknown rocks on the way.
Use the rover arm to pick up a soil sample

## Slide 3: Demo Intro
Path Planning
(Navigation Toolbox)
Mars Rover Navigation App
(MATLAB App)

## Slide 4: Demo Intro
Camera Sensor
(MATLAB Graphics)
Rock Detection
(Deep Learning)
Obstacle Avoidance

## Slide 6
Simulink Model
Object Detector
(DL Toolbox + Image Processing Toolbox)
Rock Depth Estimation
(CV Toolbox)
Rover and Arm Control
(Robotics System Toolbox + Simscape Multibody)
Rover Model
(Simscape Multibody)
Obstacle Avoidance
(Navigation Toolbox)

## Slide 7: Rover Model

## Slide 8: Rover Model
6-wheeled vehicle
6-DOF robotic arm
Rocker bogie suspension
Nav cams – left and right cameras with stereo vision
Ackerman steering
Max velocity ( ~0.1 mph)

## Slide 9: Estimating Rover Position
Simplified sensor models
Discrete-Time Kalman Filter
Rover XY Position
Estimates
Kalman Filter for fusing multi-sensor measurement
Thanks to
Ameya Godbole

## Slide 10: Virtual Mars Terrain
Rocks
Ditches
Steep Terrain
40 x 40 m Map
Contact mechanics with the 6 rover wheels
MATLAB used to get the grid data from STL
Rocks and ditches added manually editing the terrain Z height
Grid surface block

## Slide 11: Path Tracking Controller
Target direction ()
Bicycle steering
angle ()
Desired steering angles
Desired wheel speeds
Desired chassis
linear velocity
Look ahead distance
Planar Kinematic Model

## Slide 12: Perception Module

## Slide 13: Perception Module : Navigation Cameras
Right Nav Cam
Left Nav Cam
Pitch
Pan
Scene update and image captures
Object Detector
Rock Depth Estimation

## Slide 14: Navigation Cameras : Scene
Left and right camera image frames are needed during simulation for many perception algorithms , like for 3D mapping using stereo vision , for object detection , visual odometry.
Simscape Multibody limitation : It can visualize the view as seen by the cameras but can’t provide the image frames during the simulation for any image processing.
So, what are the options : Unreal engine, Simulink 3D animation.
But this has overhead and probably requires time to setup a scene
Chosen approach : Scene plotting using MATLAB Graphics

## Slide 15: Navigation Cameras : Scene plotting using MATLAB Graphics
Scene has no moving obstacles for this application
Ease of data transfer between MATLAB and Simulink.
Low overhead
Plot terrain using >>surf()
Move the camera within a scene using >>campos

## Slide 16
MATLAB Graphics Scene
Mech Explorer

## Slide 17
Preprocessing
Data
Object Detection Network
Train Network
Validate
Obstacle Detection using Deep Learning
10K training images
Labeled using binary masking
Simscape runtime parameters used to update rover poses , camera pitch and pan angles.
MATLAB used to automate camera frame captures
YOLOv2 : You Only Look Once object detector
>> trainYOLOv2ObjectDetector()
Thanks to Deep Learning QEs :
Antonio Hidalgo and
Gabija Marsalkaite

## Slide 18: Obstacle Depth Estimation using Stereovision
Stereo vision is the process of extracting 3D information from multiple 2D views of a scene
Stereo Camera Calibration
Geometric camera calibration, estimates the parameters of a lens like focal length and the distance between 2 stereo cameras etc.
>>stereoCameraCalibrator
Disparity Map
The amount of horizontal distance between the object in image L and image R (the disparity) is inversely proportional to the distance from the observer (depth)
Reconstruct 3D scene
Disparity Map
cameraParams
+
Computer Vision Toolbox

## Slide 19: Depth Estimation
+
6.37 meters
Reconstructed scene - 3D point cloud (in camera reference frame)
Distance of detected rock wrt camera ref frame

## Slide 20: Path Planning

## Slide 21
Path Planning : Offline planning
Steep terrain points
Hazardous ditches
Hazardous known rocks
Hazardous Unknown rock
3D terrain map and some obstacles are assumed to be known using offline mapping / terrain analysis.
Hybrid A star planner (Nav Toolbox)
???

## Slide 22
Path Planning : Obstacle avoidance and Online planning
Detect Rocks + Estimate their location w.r.t rover
Check if any detected rock is on the currently planned path and is less than 3.5 m away
Transform location of rock on path to global map
Update obstacle map
Original Planned Path (using offline planner)
Trained object (rock) detector + stereovision
Replan from current location to goal location
Using hybrid A star planner
Rock detected on original path
Obstacles known
to the offline planner
YES
NO
No op

## Slide 23: Mars Rover Arm
Six degrees of freedom
Waypoints define end effector trajectory
  Position, orientation relative to arm base
  Inverse kinematics used to find joint angles
R1
R2
R3
R4
R5
R6
Drill Tip Waypoints
Sample
Joint Angles
Trajectory

## Slide 24: Sample Pick Up
Variable Mass blocks for generating a soil sample
Joint Engagement/Disengagement for sample collection

## Slide 25: Results

## Slide 26: GHC 22 Event
‘AI takes Autonomous Navigation to Mars and Beyond’ workshop
~400 participants
Thanks for your support !
Kritika Ramani (QE)
Maria Gavilan-Alfonso (EduMarketing)
Chinmayi Lanka (QE)
Sara Nambi (Dev)
Ameya Godbole (QE)

## Slide 27: Technical Resources
Demo Location : https://insidelabs-git.mathworks.com/hupadhya/autonomous-mars-rover
  >> mars_rover_startup;
Rover model details and controls algorithms used:
  https://www.mathworks.com/help/sm/ug/mars_rover.html
  https://www.mathworks.com/matlabcentral/fileexchange/105700-mars-rover-model-in-simscape/?s_tid=LandingPageTabfx
  Pure Pursuit controller : https://www.mathworks.com/help/robotics/ug/pure-pursuit-controller.html
Path planner used:
  Hybrid A star planner https://www.mathworks.com/help/nav/ref/plannerhybridastar.html
Deep Learning algorithm used:
  Yolov2: https://www.mathworks.com/help/deeplearning/ug/object-detection-using-yolo-v2.html
  https://www.mathworks.com/help/vision/ug/getting-started-with-object-detection-using-deep-learning.html
4.Stereo Vision algorithm:
  https://www.mathworks.com/help/vision/ug/depth-estimation-from-stereo-video.html
  https://www.mathworks.com/help/vision/ug/using-the-stereo-camera-calibrator-app.html
Details regarding how the detector network was constructed/trained - GHC_yolov2.docx

## Slide 28: Thank You !

## Slide 29
Other useful tricks
Fast restart mode for quick restart of simulation
Update graphics in MATLAB app while Simulink is running by attaching a listener
>> add_exec_event_listener